## Slide 1
ISO 9001
Certified
Release Date 4.1.16
SHANGHAI YOUWEI’S
Screw Conveyors
Systems and Solutions for the
Hygienic and Safe Handling of Powders, Bulk Materials
for the Chemical, Food, Pharmaceutical and Pigment Industries
www.uv-powder.com

## Slide 2
Shanghai Youwei Mechanical and Electrical Co., Ltd. was established in 2011. It is a production-oriented processing enterprise specializing in powder unpacking, transportation, weighing, metering, batching and packaging equipment manufacturing. The company's registered capital is 12 million. The company has two processing bases in Zhangjiagang City and Qidong City, with a plant area of nearly 8,000 square meters.
With more than ten years of experience in the field of material handling automation, we have always been customer-oriented and have independently developed small bag feeding stations, ton bag unpacking machines, vacuum feeders, weighing and metering ingredients, ton bag packaging machines and other equipment. We have rich industry experience in the food ingredients industry, lithium battery anode and cathode industry, and pharmaceutical intermediates industry.
The company adheres to the spirit of integrity, pragmatism and innovation, and relies on rich technology development experience to provide high-quality systematic solutions to all types of users, and work hand in hand with users to create a better future.
About Us
About Us
Some customers

## Slide 3
Screw Conveyors
SCREW CONVEYOR BASICS
1
The SHANGHAI YOUWEI’S Screw Conveyor Engineering Guide will provide assistance in the design of a screw conveyor or system, yielding optimum performance and efficiency.
Primary considerations for the selection of a screw conveyor are:
Type and condition of the bulk material to be conveyed including maximum particle size and specific bulk density
Capacity or feed rate of bulk material to be conveyed expressed in pounds per hour, tons per hour, or cubic feet per hour
Required distance and incline the bulk material is to be conveyed
Design conditions such as materials of construction, inlet feed conditions and operating temperature
The Engineering Guide provides the necessary information for selecting a screw conveyor in a series of five steps. These steps are arranged in logical order and are divided into separate sections for simplicity.
The five steps are:
Establish characteristics of the bulk material to be conveyed.
Determine conveyor size and speed based on capacity.
Calculate horsepower requirements.
Verify torque rating of components.
Select conveyor components.
Typical YOUWEI’S Screw Conveyor

## Slide 4
TYPES OF SCREW CONVEYORS
Horizontal Screw Conveyors
Horizontal screw conveyors are the most widely used type of screw conveyor. Used to convey bulk materials from one part of a process to another, horizontal screw conveyors are available in a wide range of sizes, lengths, configurations and materials of construction.
Screw conveyors are typically designed to convey bulk materials at 15, 30 or 45-percent trough loading, depending upon material characteristics of the specific bulk material. As a general rule, trough loading of 45-percent can be used for light, free-flowing and non-abrasive bulk materials. Trough loadings of 15 and 30-percent are typically used for denser, sluggish and more abrasive bulk materials.
The inlet of a screw conveyor is always control fed by another device such as:
Screw Conveyor
Screw Feeder
Belt Conveyor
Rotary Airlock
Volumetric or Gravimetric Feeder
The recommended location for the drive unit is on the discharge end of a screw conveyor which pulls the bulk material to the drive end. With this arrangement, each screw section is put in tension as the bulk material is conveyed toward the discharge of a screw conveyor, reducing wear and fatigue on the conveyor components.
Advantages of Using Screw Conveyors
Ideal for conveying dry to semi-fluid bulk materials – free flowing to sluggish
Cost-effective when compared to other conveying devices such as belt, pneumatic or aero- mechanical
Efficiently distributes bulk materials to various locations using multiple inlet and discharge points
Totally enclosed for dusty, corrosive or hazardous environments
Screw Conveyors

## Slide 5
TYPES OF SCREW CONVEYORS
Inclined Screw Conveyors
Inclined screw conveyors typically operate from slightly above the horizontal position to 45-degrees from the horizontal position. Above 45-degrees an inclined screw conveyor is considered a
vertical screw conveyor and must be designed in accordance with the YOUWEI Engineering Guide for Vertical Screw Conveyors. As the degree of incline increases, conveying efficiency is reduced and horsepower requirements increase due to the effects of gravity and bulk material fall back.
Conveying efficiency is affected by angle of incline, characteristics of the specific bulk material, type of screw conveyor trough and screw pitch. YOUWEI recommends designing screw conveyors using the lowest possible degree of incline for maximum efficiency.
The following are design and construction features to consider when designing an inclined screw conveyor:
Incline Up to 10-Degrees – Loss in conveying efficiency is minimal on inclines up to 10-degrees. A screw conveyor with U-trough and full pitch screw is sufficient for most applications. Loss in efficiency can be overcome by increasing the speed of the screw
conveyor, increasing the diameter of the screw conveyor or reducing the pitch of the screw.
Incline Between 10 and 20-Degrees – Loss in conveying efficiency is typically between 10 and 40-percent on inclines up to 20-degrees. A screw conveyor with U-trough and 2/3-pitch screw is sufficient for most applications. Loss in efficiency can also be overcome by increasing the speed or the diameter of the screw conveyor. Additional horsepower is required to overcome gravity and bulk material fall back.
Incline Between 20 and 30-Degrees – Loss in conveying efficiency is typically between 10 and 70-percent on inclines up to 30-degrees. A screw conveyor with tubular housing and reduced pitch screw (1/2 or 2/3) is recommended for most applications. Loss in efficiency can also be overcome by increasing the speed or the diameter of the screw conveyor. Additional horsepower is required to overcome gravity and bulk material fall back.
Incline Between 30 and 45-Degrees – Loss in conveying efficiency is typically between 30 and 90-percent on inclines up to 45-degrees. A screw conveyor with tubular housing and reduced pitch screw (1/2 or 2/3) and larger diameter is recommended for most applications. Increasing the speed of the screw conveyor is also required. Additional horsepower is required to overcome gravity and bulk material fall back.
3
Screw Conveyors

## Slide 6
TYPES OF SCREW CONVEYORS
Shaftless Screw Conveyors
Bulk materials discharged from centrifuges, filter presses or mixers can easily be conveyed using a YOUWEI’S Shaftless Screw Conveyor. Our shaftless design provides a non-clogging conveying surface that allows difficult-to-convey materials to become easy-to-convey. The perfect solution for handling bulk materials with high moisture content is the YOUWEI Shaftless Screw Conveyor.
Advantages of Shaftless Screw Conveyors
Ideal for handling sticky and sluggish bulk materials
Improved conveying efficiency when compared to other types of conveyors
Allows greater flexibility for plant layout due to configurations available
Internal bearings are eliminated
UV Shaftless Screw Conveyors are successfully used throughout the chemical, food, minerals processing and wastewater treatment industries for conveying everything from catalysts to dewatered biosolids.
UV developed the industry standards for shaftless screw conveyors and continues to create new and improved design standards. Our high strength alloy spirals are the hardest, strongest and
toughest in the industry. For more information regarding shaftless screw conveyors consult the UV Shaftless Screw Conveyor Engineering Guide located on our website.
5
Screw Conveyors

## Slide 7
TYPES OF SCREW CONVEYORS
Vertical Screw Conveyors
Vertical screw conveyors are a very efficient method for elevating a variety of bulk materials at very steep inclines or completely vertical. UV considers any screw conveyor located on an incline over 45-degrees to be a vertical screw conveyor. The compact design allows for the vertical screw conveyor to fit into almost any plant layout. With a minimum number of moving parts, the vertical screw conveyor is a cost-effective and dependable
component of any bulk material handling process.
Advantages of Vertical Screw Conveyors
Ideal for handling dry to semi-fluid materials
Capacities up to 6,000 cubic feet per hour.
Ability to elevate bulk materials up to 30-feet without use of internal bearings.
Totally enclosed design for dust and vapor-tight requirements.
UV designs and supplies vertical screw conveyors to meet the needs of many industries, such as chemical, minerals processing, food, wood products and wastewater treatment. For example, our unique shaftless vertical screw conveyor design is used in many wastewater treatment facilities for elevating dewatered biosolids.
UV Vertical Screw Conveyors are available in many configurations. Inlet sections can be offset to either side or can be in-line. Horizontal feed conveyors are required to accurately meter bulk materials directly to the vertical conveyor’s inlet for maximum efficiency.
For more information regarding vertical screw conveyors, consult the UV Vertical Screw Conveyor Engineering Guide located on our website.
6
Screw Conveyors

## Slide 8
TYPES OF SCREW FEEDERS
Screw Feeders
Screw feeders are designed to meter bulk materials and are typically located at the beginning of a process. Capacity or feed rate can be accurately controlled with screw feeders. Variable speed drives improve metering accuracy and can provide a wide range of feed rates. Screw feeders are available in a variety of sizes, lengths, configurations and materials of construction.
The inlet of a screw feeder is always flood loaded (100-percent). A screw feeder is typically mounted directly to a:
Hopper – Square or rectangular in shape with sloped bottom and limited storage capacity
Bin – Square or rectangular in shape with sloped bottom and large storage capacity
Silo – Cylindrical in shape with cone or mass-flow bottom and large storage capacity
Several factors must be considered when designing a screw feeder, including:
Flow characteristics of bulk material being stored and metered
Density of bulk material in both stored and metered condition
Maximum and minimum capacity or feed rate of process
Bulk material size with screen analysis
Width and length of screw feeder inlet opening
Overall length of screw feeder
Height of bulk material in hopper, bin or silo
With the screw feeder inlet flood loaded (100-percent), the design of the screw in the inlet area and the screw speed determine the desired capacity or feed rate.
Most screw feeders are less than 20-feet in length because the use of internal hanger bearings is not recommended. In most applications a short screw feeder will meter a bulk material to a screw conveyor for transfer to the next step of the process.
UV designs and manufactures three types of screw feeders:
Variable or Stepped Pitch – The pitch of the screw varies from shorter to longer as the screw progresses toward the discharge of the screw feeder. With variable pitch, every pitch increases
in length in the inlet section creating more available volume for addition of bulk materials from the hopper. With stepped pitch the flight pitch changes in increments. For example, a stepped pitch screw feeder may have 2-feet of 1/3 pitch, then 2-feet of 2/3 pitch in the inlet section.
7
Screw Conveyors

## Slide 9
Tapered Outside Diameter – The outside diameter of the screw is tapered from the rear of the inlet opening to the shroud creating more available volume for addition of bulk materials from the hopper.
Mass Flow – The mass flow design was developed by Jenike & Johanson and is a combination of variable pitch and tapered inside diameter. A tapered cone is located on the center pipe of the screw from the rear of the inlet opening to approximately the center of the inlet opening. Short pitch flights are mounted on the cone creating available volume for addition of bulk materials from the hopper. Variable pitch is then added to the screw starting where the cone ends and continuing to the discharge.
TYPES OF SCREW FEEDERS
Mass flow in a hopper
Screw feeders can be composed of one, two or virtually any number of screws. A screw feeder with multiple screws is considered a live bottom screw feeder.
8
Screw Conveyors
TYPES OF SCREW FEEDERS

## Slide 10
1
3
4
5
2
6
7
Inlet opening matches bin or hopper discharge.
Feeder Shroud prevents material flooding.
Twin mass flow, variable pitch screw feeder permits even draw off of material.
Twin screw trough.
Discharge opening.
Solid shafting transmits rotary motion to gear reducer.
Independent gear boxes to drive each screw.
Basic Screw Feeder Design
It is not recommended to design screw feeders with uniform outside diameter and constant pitch because bulk materials will fill the screw from the rear of the inlet opening first, creating rat-holing, stagnant material and possible bridging of bulk materials above the screw feeder. To draw bulk materials evenly across the full length of the inlet each flight must increase in available volume as the screw progresses towards the discharge of the screw feeder. Variable pitch, tapered outside diameter (OD) or mass flow screw design is required.
9
Screw Conveyors

## Slide 11
Live Bottom Screw Feeder
Live bottom screw feeders are designed for use on large silos, bins and hoppers with large discharge openings. The live bottom screw feeder utilizes multiple feeder screws in tandem to create a “live bottom” to prevent bridging. Bulk materials are metered and drawn out equally from the full width and length of the inlet opening. Live bottom screw feeders are used on bulk materials which tend to pack or bridge easily.
When designing a screw feeder, every application is unique. For this reason, please consult KWS Engineering for proper recommendations concerning your particular needs.
TYPES OF SCREW FEEDERS
OTHER TYPES OF SCREW FEEDERS
Multiple Diameter Screw Feeder/Conveyor
Multiple Diameter Screw Feeder/Conveyors consist of a screw feeder with an extension conveyor. A smaller diameter screw feeder is located under a hopper, bin or silo and is flood loaded. The screw feeder meters the bulk material to the larger diameter extension conveyor. When the bulk material reaches the extension conveyor the trough loading decreases and the bulk material is conveyed to the discharge. Hanger bearings are allowed in the extension conveyor as long as the trough loading is below 45-percent.
Screw Conveyors

## Slide 12
FACTORS INFLUENCING SCREW CONVEYOR DESIGN
Abrasiveness, Corrosiveness and Flowability
The Bulk Material Table also presents the relative abrasiveness, corrosiveness and flowability of the bulk materials listed. These characteristics, as well as other special aspects of bulk materials, are given further consideration in the Component Selection Section. The
nomenclature used in the Bulk Material Table are listed below.
NOTE: Some bulk materials, while they are not corrosive under “normal” conditions, may become corrosive when heated or in the presence of moisture.
Special Characteristics Notes Notable unusual bulk material characteristics are listed by alphabetical codes in the last column of the Bulk Material Table where applicable. An explanation of these numerical codes
is shown on the right and in the Bulk Materials Characteristics section.
Description | I | II | III | IV
Abrasiveness | Mildly Abrasive | Moderately Abrasive | Extremely Abrasive | —
Corrosiveness | Not Corrosive | Mildly Corrosive | Highly Corrosive | —
Flowability | Very Free Flowing | Free Flowing | Average Flowability | Sluggish
 | Angle of Repose |  |  | 
 | To 30° | 30° - 45° | 30° - 45° | Beyond 45°
A | Builds Up and Hardens
B | Generates Static Electricity
C | Decomposes—Deteriorates in Storage
D | Flammability
E | Becomes Plastic or Tends to Soften
F | Very Dusty
G | Aerates and Becomes Fluid
H | Explosiveness
I | Stickiness—Adhesion
J | Contaminable, Affecting Use
K | Degradable, Affecting Use
L | Gives Off Harmful or Toxic Gas or Fumes
M | Hygroscopic
N | Interlocks, Mats, or Agglomerates
O | Oils Present
P | Packs Under Pressure
Q | Very Light and Fluffy—May Be Windswept
R | Elevated Temperature
V | May Be Conveyed In a Vertical Screw Conveyor
• | Consult UV Engineering Department
Screw Conveyors

## Slide 13
FACTORS INFLUENCING SCREW CONVEYOR DESIGN
Ammonium Sulfate
Abrasive Bulk Materials To prevent excessive wear in screw conveyors handling abrasive bulk materials, use abrasion-resistant alloys like AR235, AR400, AR500, TriBraze, or chromium carbide overlay. Consider hardsurfacing the carrying face with a weld-on material. To minimize wear, reduce trough loading and screw conveyor speed when dealing with abrasives.
Highly Corrosive For handling highly corrosive bulk materials, use corrosion-resistant alloys like 304, 310, 316, 410, and 430 stainless steels. High nickel alloys such as Inconel, Monel, and Hastalloy are also suitable choices for fabrication in such environments.
Mildly Corrosive For mildly corrosive bulk materials or those prone to corrosion, use corrosion-resistant alloys like 304 and 316 stainless steels for screw conveyor fabrication.
Builds Up and Hardens (A) For materials that build up and harden, use screw conveyors with close clearance between screw and trough to prevent buildup. High-torque drive units, including carbide tip teeth, are needed to shear through hardened bulk materials that tend to pack and absorb moisture.
Quartz
Copper Sulfate
Drilling Sludge
Screw Conveyors
Bentonite
Generates Static Electricity (B) To address static electricity in screw conveyors conveying plastic pellets, ground the trough at multiple points. Additionally, minimize trough loading and reduce operating speeds to mitigate static buildup.
Ground Meat
Decomposes – Deteriorates in Storage (C) Bulk materials prone to decomposition or deterioration must be promptly discharged and processed from hoppers, bins, or silos to prevent spoilage. Designing screw feeders and conveyors should consider the characteristics of such materials to ensure effective handling.
Hay
Flammability (D) To mitigate fire risk in handling flammable bulk materials, design screw conveyors with non-sparking materials. Use pressure-tight troughs with mechanical shaft seals to prevent oxygen entry, and consider purging the conveyor with inert gases like nitrogen for added safety.

## Slide 14
Very Dusty (F)
Some bulk materials can become very dusty and leak out from screw conveyors. These dusty bulk materials can become
a hazard or even be explosive. Screw conveyors must be completely sealed with special shaft seals to contain the dusty
bulk material. Design of screw conveyor troughs or housings depends on the severity of the hazard.
Aerates and Becomes Fluid (G)
Fluidizing bulk materials will aerate and tend to flow like liquids when conveyed. The “as conveyed” bulk density is much lower than the static or packed bulk density. In some cases the fluidized bulk material will flood and “run like water” with the loss of control of capacity or feed rate. Trough
loading will increase causing the flooding of downstream equipment. Lower trough loading and slower screw speeds are recommended to reduce the chance of aeration of the bulk material.
Explosiveness (H)
Explosive bulk materials will ignite when oxygen and an ignition source are present. Screw conveyors can be designed with non-sparking materials to eliminate a possible ignition source. Pressure tight troughs or housings with mechanical shaft seals will keep oxygen from entering the screw conveyor. The inside of the screw conveyor trough or housing can be purged with an inert gas such as nitrogen. Explosion venting is also an option for relieving pressure due to an explosion.
Stickiness - Adhesion (I)
Viscous or sticky bulk materials contain a high percentage of moisture or oil and are difficult to convey. Sticky bulk materials tend to stick to the center pipe of a screw conveyor where
the flight is welded to the center pipe. Ribbon flighting is an excellent choice for handling sticky bulk materials. Shaftless screw conveyors provide even better performance than shafted conveyors with ribbon flighting.
Rice Grits
Powdered Milk
Aluminum Oxide
Hydrated Lime
Screw Conveyors

## Slide 15
Screw Conveyors
SIZE | Chassis outer diameter (MM) | Conveying capacity (KG/H） | Speed (R/MIN) | Motor Power (kw)
LX-100 | 108 | 20-500 | 24-132 | 0.75
LX-125 | 133 | 50-1000 | 24-132 | 1.1
LX-150 | 159 | 200-2000 | 24-132 | 1.5
LX-200 | 219 | 400-4000 | 24-132 | 2.2
LX-250 | 254 | 500-6000 | 24-132 | 2.2
LX-300 | 315 | 600-9000 | 24-132 | 4
1. The conveying capacity is related to the working angle and length as well as the nature of the material. The above conveying capacity is for reference only. 2. A debug motor can be selected according to customer requirements and equipped with frequency conversion speed regulation. 3. The above table shows the standard series product models. Special specifications for special products require consultation and separate design. |  |  |  | 
Screw conveyors are mainly used for horizontal transportation and vertical lifting of various powdery, granular and small pieces of loose materials. This equipment has the characteristics of small spiral diameter, high rotation speed, large conveying capacity, high precision, and good conveying conditions. It is simple to operate and maintain; for one conveyor, it can be loaded at multiple points or unloaded at multiple points on the conveying line; during the process of conveying materials, materials can be mixed, stirred or cooled at the same time, and the rigidity of the shell can withstand a certain external force. . The conveyor shell is made of high-quality seamless pipes and flange connections. It has good overall rigidity and large load-bearing capacity. It can be transported continuously whether horizontally or at a large angle during transportation. The working position and working state can be selected at will, disassembled, assembled and moved. convenient
Device parameters:

## Slide 16
Screw Conveyors
Our Experienced engineers meticulously design
custom screw conveyors
on cutting-edge at our company,
ensuring precision and efficiency.
Your unique specifications are transformed into
high-performance conveyor solutions
, reflecting our commitment to delivering tailored
excellence for your material handling needs
Experience precision and safety with
our skilled workforce as they expertly
weld design screw conveyors.
Meticulously crafted components
meet the highest standards, ensuring
reliability and efficiency in material
handling solutions. Your satisfaction
is our priority, reflecting our unwavering
commitment to excellence in every weld.
Ensuring the seamless integration of
components, At every stage, our
commitment to crafting superior material
handling solutions shines through,
reflecting our dedication to delivering
excellence to our valued customers.
Our skilled worker meticulously measures every detail of your custom-designed screw conveyor, ensuring precision and excellence. Trust us for tailor-made solutions that exceed expectations in material handling.

## Slide 17
Screw Conveyors
F Multi-output bottom
F Stainless steel 304L / 316L design
F Modular design
Advantages
F End bearing with shaft sealing
F Conveyor roll end bearing
F Intermediate bearing

## Slide 18
Screw Conveyors
Bulk Material Handling: Screw conveyors excel at moving large volumes of bulk materials like grains, powders, pellets, and even semi-solids.
Stainless Steel: Used for corrosive or contaminable materials, with 304 and 316 being popular choices.
Controlled Flow: The rotating screw regulates the material flow rate, ensuring consistent and predictable delivery

## Slide 19
Screw Conveyors
Diverse Material Compatibility: They can handle a wide range of materials, from free-flowing powders to sticky and abrasive substances.
Seamless Integration: Designed for seamless integration into existing systems, our screw conveyors facilitate smooth material flow, contributing to operational efficiency.
Advanced Technology: Leveraging cutting-edge technology, our screw conveyors are equipped with state-of-the-art components, enhancing performance and reducing maintenance requirements.
Robust Shaft Construction: Our screw conveyors feature a robust shaft design, crafted from high-strength materials to withstand heavy loads and resist deformation.

## Slide 20
Bulk Material | Maximum Particle Size (in.) | Bulk Density (lbs/ft³) | % Trough Loading | Material Factor (MF) | Component /Bearing Series | Abrasive- ness | Corrosive- ness | Flowability | Special Notes
Bonechar | -1/8 | 27-40 | 30A | 1.6 | A1-A2 | I | I | III | 
Bonemeal | -1/8 | 50-60 | 30A | 1.7 | B4 | I | I | III | 
Bones, Crushed | -3 | 35-50 | 30A | 2.0 | B4 | I | I | IV | 
Bones, Ground | -1/8 | 50 | 30A | 1.7 | B4 | I | I | III | 
Bones, Whole | Irregular | 35-50 | 30A | 3.0 | B4 | I | I | IV | N
Borate of Lime | -100M | 60 | 30A | 0.6 | A1-A2-A3 | I | I | III | •
Borax Lumps | 1 1/2 to 2 | 55-60 | 30A | 1.8 | B4 | I | I | III | 
Borax Lumps | 2 to 3 | 60-70 | 30A | 2.0 | B4 | I | I | III | 
Borax, Fines | -1/8 | 45-55 | 45 | 0.7 | C4 | I | II | II | 
Borax, Screenings | -1/2 | 55-60 | 30A | 1.5 | B4 | I | I | III | 
Boric Acid | -1/8 | 55 | 45 | 0.8 | C4 | I | II | II | 
Boron | -100M | 75 | 15 | 1.0 | B4 | III | I | III | 
Bran, Rice—Rye— Wheat | -1/8 | 16-20 | 30A | 0.5 | A1-A2-A3 | I | I | III | H, Q
Braunite (Manganese Oxide) | -100M | 120 | 30B | 2.0 | B4 | II | I | III | 
Bread, Crumbs | -1/8 | 20-25 | 30A | 0.6 | A1-A2-A3 | I | I | III | J,K
Brewers Grain, Spent, Dry | -1/2 | 14-30 | 30A | 0.5 | A1-A2-A3 | I | I | IV | 
Brewers Grain, Spent, Wet | -1/2 | 55-60 | 30A | 0.8 | D3 | I | II | IV | 
Brick, Ground | -1/8 | 100-120 | 15 | 2.2 | C4 | III | I | III | 
Bronze Chips | -1/8 | 30-50 | 30A | 2.0 | B4 | I | I | IV | 
Buckwheat | -1/8 | 37-42 | 45 | 0.4 | A1-A2-A3 | I | I | II | H
Calcine, Flour | -100M | 75-85 | 30A | 0.7 | A1-A2-A3 | I | I | III | 
Calcium Carbide | -3 | 70-90 | 30A | 2.0 | B4 | I | I | II | H
Calcium Lactate | -3 | 26-29 | 30A | 0.6 | B1-B2 | I | II | IV | K, L, P
Calcium Magnesium Carbonate | + 1/2 | 90-100 | 30B | 2.0 | B4 | II | I | II | 
Calcium Phosphate | -100M | 40-50 | 30A | 1.6 | A1-A2-A3 | I | I | IV | 
Carbon, Activated, Dry, Fine | -1/8 | 8-20 | 30A | 1.2 | B4 | I | I | II | K, •
Carbon Black, Fine | -100M | 4-7 | 30A | 0.4 | A2 | I | I | III | P, Q, •
Carbon Black, Pelleted | -1/8 | 20-25 | 45 | • | • | I | • | I | M, P, •
Carborundum* | -3 | 100 | 15 | 3.0 | C4 | III | I | II | 
Casein | -1/8 | 36 | 30A | 1.6 | B4 | I | I | III | 
Cashew, Nuts | -1/2 | 32-37 | 30A | 0.7 | B4 | I | I | IV | 
Cast Iron, Chips | -1/2 | 130-200 | 30A | 4.0 | B4 | I | I | IV | 
Caustic Soda (Sodium Hydroxide) | -1/8 | 88 | 30A | 1.8 | D4 | I | III | III | L, M
Caustic Soda, Flakes (Sodium Hydroxide) | -1/2 | 47 | 30A | 1.5 | D4 | I | III | IV | K, L, M, P
Screw Conveyors
Bulk Densities of some Materials

## Slide 21
Bulk Material | Maximum Particle Size (in.) | Bulk Density (lbs/ft³) | % Trough Loading | Material Factor (MF) | Component /Bearing Series | Abrasive- ness | Corrosive- ness | Flowability | Special Notes
Celite (Diatomaceous Earth) | -1/64 | 11-17 | 30B | 1.6 | C4 | II | I | III | G, P, Q, •
Cement, Aerated (Portland) | -100M | 60-75 | 30B | 1.4 | B4 | II | I | I | G
Cement, Clinker | -3 | 75-95 | 30B | 1.8 | D4 | II | I | III | 
Cement, Mortar | -1/8 | 133 | 30A | 3.0 | C4 | I | I | III | K
Cement, Portland | -100M | 94 | 30B | 1.4 | B4 | II | I | II | G
Cerrusite (Lead Carbonate) | -1/64 | 240-260 | 30A | 1.0 | B4 | I | I | III | G, L
Chalk, Crushed | -3 | 75-95 | 30A | 1.9 | B4 | I | I | II | P
Chalk, Ground | -100M | 67-75 | 45 | 1.4 | B4 | I | I | II | G, P, Q
Charcoal, Ground | -100M | 18-28 | 30A | 1.2 | B4 | I | I | IV | H
Charcoal, Lumps | -3 | 18-28 | 30A | 1.4 | B4 | I | I | IV | H, K
Chips, Pulpwood | +1/2 | 12-25 | 30A | 1.0 | B1 | I | I | III | N, Q
Chocolate, Cake, Pressed | -3 | 40-45 | 30A | 1.5 | B2 | I | I | II | 
Chrome Ore | -3 | 125-140 | 30B | 2.5 | C4 | II | I | III | 
Cinders, Blast Furnace | -3 | 57 | 30B | 1.9 | D4 | II | II | III | 
Cinders, Coal | -3 | 40 | 30B | 1.8 | D4 | II | II | III | 
Clay, Brick, Dry, Fines | -1/2 | 100-120 | 30B | 2.0 | C4 | II | I | III | 
Clay, Calcined | -1/8 | 80-100 | 30B | 2.4 | C4 | II | I | III | 
Clay, Ceramic, Dry, Fines | -100M | 60-80 | 30A | 1.5 | A1-A2-A3 | I | I | III | J
Clay, Dry, Lumpy | -3 | 60-75 | 30A | 1.8 | B4 | I | I | III | 
Clinker, Cement | -3 | 75-95 | 30B | 1.8 | D4 | II | I | III | 
Clover, Seed | -1/8 | 45-48 | 45 | 0.4 | A1-A2-A3 | I | I | II | H
Coal, Anthracite (Culm and River) | -1/8 | 55-61 | 30A | 1.0 | B1-B2 | I | II | III | 
Coal, Anthracite, Sized | -1/2 | 49-61 | 45 | 1.0 | B1-B2 | I | I | II | 
Coal, Bituminous, Mined | -3 | 40-60 | 30A | 0.9 | A1-A2 | I | I | III | F, H, P, Q
Coal, Bituminous, Mined, Sized | -3 | 45-55 | 30A | 1.0 | A1-A2 | I | I | III | H, K, N
Coal, Bituminous, Mined, Slack | -1/2 | 43-50 | 30A | 0.9 | B1-B2 | I | II | IV | H
Coal, Lignite | -3 | 37-45 | 30A | 1.0 | B4 | I | II | III | H
Cocoa, Beans | -1/2 | 30-45 | 45 | 0.5 | A1-A2 | I | I | II | K
Cocoa, Nibs | -1/2 | 35 | 45 | 0.5 | B4 | I | I | II | 
Cocoa, Powdered | -100M | 30-35 | 30A | 0.9 | A2 | I | I | IV | G, P, Q
Coconut | Shredded | 20-22 | 30A | 1.5 | B2 | I | I | IV | 
Coffee, Beans, Green | -1/2 | 25-32 | 45 | 0.5 | A1-A2 | I | I | II | J, K
Screw Conveyors
Bulk Densities of some Materials

## Slide 22
Invest in your operators' well-being and boost your production efficiency with SHANGHAI YOUWEI Contact us today to learn more!
High cost performance-super high quality, super low price
Lifetime service
Powered by technology and survive by quality
Shanghai Youwei Powder Equipment Co., Ltd.
Address: No. 351, Sizhuan Highway, Songjiang District, Shanghai
Website: www.uv-powder.com
Mail:anas@uv-powder.com
Service supervision hotline: +1(213)569-6682